## Slide 1: Theoretical and Experimental Investigation of Ag and Pt-decorated In2O3 Gas Sensors
MSc. Gustavo Sanghikian Marques dos Santos (Unesp / UJI)
Supervisors:
Prof. Dr. Diogo Paschoalini Volanti (Unesp – Brazil)
Prof. Dr. Juan Manuel Andrés Bort (UJI – Spain)

## Slide 2: Academic Background
2018 – 2022: Bachelor’s degree in Chemistry
2022 – 2023: Master’s degree in Chemistry
October/2023 – now: PhD Student in Chemistry
Research focused on the synthesis, characterization, and application of semiconducting metal oxides for gas sensing applications (ZnO, Co3O4, In2O3...).
São Paulo State University (Unesp – Brazil)

## Slide 3
São Paulo State University (Unesp) Institute of Biosciences, Humanities and Exact Sciences (IBILCE) – São José do Rio Preto, SP - Brazil
Academic Background

## Slide 4
Academic Background
Laboratory of Materials for Sustainability (LabMatSus), led by Prof. Dr. Diogo Paschoalini Volanti

## Slide 5
Academic Background
Theoretical and Computational Chemistry (QTC), led by Prof. Dr. Juan Manuel Andrés Bort

## Slide 6: Published Works
[1] Gustavo S.M. Santos, Bruna S. de Sá, Tarcísio M. Perfecto, Diogo P. Volanti, MOF-derived Co3O4-ZnO heterostructure for 3-methyl-1-butanol detection, Sensors and Actuators B: Chemical, Volume 408, 2024, 135533, ISSN 0925 4005, https://doi.org/10.1016/j.snb.2024.135533.
Source: Santos et al. 2024 [1]

## Slide 7: Published Works
[2] Gustavo Sanghikian Marques dos Santos, Reinaldo dos Santos Theodoro, Gabriela Oliveira Gera, Tarcísio Micheli Perfecto, and Diogo Paschoalini Volanti. Ethyl Acetate Detection Using Mixed-Phase In2O3 Nanorods ACS Applied Nano Materials 2025 8 (22), 11458-11469 DOI: 10.1021/acsanm.5c01487
Santos et al., ACS Applied Nano Materials, 2025.
Front Cover feature in ACS Applied Nano Materials
June 6, 2025 – Vol. 8, N. 22

## Slide 8: Published Works
Ethyl Acetate Detection Using Mixed-Phase In2O3 Nanorods

## Slide 9: Published Works
Indium(III) oxide
Indium(III) oxide is an n-type SMO with a high band gap, excellent electrical conductivity, and strong adsorption of gaseous molecules;
It is widely employed in liquid crystal devices, solar cells, and gas sensors;
The stable crystal phase is the cubic bixbyite-type (bcc-In2O3 , Eg = 2.93 ± 0.15 eV), while the metastable is the rhombohedral corundum-type (rh-In2O3 , Eg = 3.02 ± 0.15 eV) (Li et al., 2014).
cubic bixbyite-type
(bcc-In2O3)
Rhombohedral corundum-type
(rh-In2O3)
9

## Slide 10: Published Works
Santos et al., ACS Applied Nano Materials, 2025.

## Slide 11: Published Works
Santos et al., ACS Applied Nano Materials, 2025.

## Slide 12: Published Works
In2O3-500 showed the best ethyl acetate sensing performance, with a maximum response of 548 at 350 °C, much higher than the other samples.
The material also exhibited high selectivity, fast response time (1.8 s), and stable detection over 2–500 ppm concentrations.
A low theoretical detection limit of ~525 ppb was estimated from linear regression analysis.
The enhanced sensing behavior is attributed to the bcc–rh heterostructure and heterojunction effect.
Santos et al., ACS Applied Nano Materials, 2025.

## Slide 13: Published Works
High sensitivity and selectivity toward ethyl acetate with a response of 548 to 100 ppm at 350 °C.
Fast response time (1.8 s), good repeatability, and potential applicability for ethyl acetate monitoring.
High operating temperatures (300-350 °C), limiting practical applications.
Long recovery time (1748.2 s).
Humidity significantly reduced the sensing performance.

## Slide 14
Noble metal nanoparticles (Ag, Pt, Pd, Au) enhance oxygen adsorption on the In2O3 surface, improving gas sensing performance.
Through the spillover effect, oxygen molecules dissociate into O⁻ species and spread across the surface, creating more active sites and electronic defects, and enabling better sensor response at lower operating temperatures.
The deposition of noble metal nanoparticles strategy:

## Slide 15
Source: Encyclopaedia Britannica

## Slide 16: Ongoing Research Activities
Surface Modelling of Cubic In2O3
(222)
(222)
(222)
In48O72
In64O96
In80O120
(111)
(211)
In96O144
In60O90
Structures obtained from Materials Project and optimized using CRYSTAL.

## Slide 17
Ag loading
Pt loading
In2O3 surface
Ag and Pt Loading Simulation on the In2O3 Surface
Ongoing Research Activities
Structures obtained from Materials Project and optimized using CRYSTAL.

## Slide 18: Ongoing Research Activities
In2O3 surface
Adsorption energy calculations of different mVOCs
Eads ​= Esurface+gas​− Esurface​− Egas​
Structures obtained from Materials Project and optimized using CRYSTAL.

## Slide 19: Final Remarks
Investigation of metal-decorated In2O3 heterostructures;
Advanced structural characterization (HRTEM, DRX, EPR);
Development of theoretical surface adsorption models;
Understanding gas sensing mechanisms at the atomic scale;
Combination of theoretical and experimental approaches regarding gas sensors, enabling the development of reliable point-of-care devices for early monitoring.

## Slide 20: Acknowledgments
grants #2024/03388-4
#2025/23707-0